## Slide 1
Risk and Scenario Based Communication System-of-System Design
JP Venter
MICSSA 2023

## Slide 2: Overview
Introduction
System Requirements
Scenarios
System Design
Results

## Slide 3: Introduction
Scenario planning is a strategic management tool that encourages managers to envision plausible future states.
Different scenarios that could influence communications systems were defined.
The influence of the scenarios of the persistence of communications systems were used to design a persistent communication system.
System makes provision for graceful degradation.
This approach ensures that provision of functionality during the ideal scenario is not downgraded to simultaneously make provision for less-than-ideal situations.

## Slide 4: System Requirements
The overall system requirement was to provide persistent communication for various geographically dispersed facilities as well as for vehicles.
Primary requirement is voice communication.
When available services such as online meetings, location sharing, and video streaming must be accommodated.
Resilience against system and power outages.

## Slide 5: Scenarios
Green Pastures:
              Stable Electricity Supply
              Stable external IP network
              External Broadband connectivity available
Fire:
              Short term disruption of electricity
              External IP network temporary outages
              Local UHF coverage gaps
Drought:
              Longer term disruption of electricity.
              Total breakdown of external IP network.
Apocalypse:
              Long term disruption of electricity
              Breakdown of all network services
              Local electronic equipment breakdown

## Slide 6: System Design
Green Pastures:
              Local repeater-based UHF radio
              UHF Radio trunked over IP network.
              4G Network based broadband for mobile users
Fire:
              Short Term UPS for important systems.
              Voice extended over Wi-Fi for UHF coverage gaps.
              Fixed and on-the-move Satellite communications
Drought:
              Longer term UPS for essential systems.
              Out-of-country ground station for satellite communications
              Satellite phones for mobile users as additional communications
Apocalypse:
              Only battery powered devices in use
              Point-to-point communications
              HF Radio

## Slide 7: Results
Proof-of-concepts
    Satellite on-the-move
    IP based voice communications
Decision Making
    Enable phased approach
    Enable partial implementation

## Slide 8: Conclusion
The scenario based approached provided a good basis for identifying various system elements necessary to provide acceptable performance over a wide range of use cases.
The scenario approach provided a means to motivate to decision makers as to the purpose of a diverse set of options.
The scenario approach further influenced the implementation plan in terms of managing the deployment of the system depending on the perceived probability of a scenario occurring.

## Slide 9: Thank you